## Slide 1: Digital Design & Computer Arch. Lab 3 Supplement: Verilog for Combinational Circuits
Prof. Onur Mutlu
ETH Zurich
Spring 2020
13 March 2020

## Slide 2: What Will We Learn?
In Lab 3, you will design more combinatorial circuits.
Convert a binary number to 7-Segment display encoding.
Implement a circuit to drive the 7-Segment display.
Show the addition result on the 7-Segment display.

## Slide 3: 7-Segment Display
A 7-segment display consists of seven separate LEDs in a single package.
Each of the seven segments is labeled using the letters a, b, c, d, e, f, g.

## Slide 4: Representing Different Numbers
We can represent different characters or digits by making particular segments glow at the same time.

## Slide 5: Binary Number to 7-Segment Encoding
As a first step, you will complete the truth table for converting a 4-bit number to a 7-segment encoding.
Note: A segment should glow when the corresponding output is logic-0.

## Slide 6: Drive the 7-Segment Display
Design a “decoder” that receives a 4-bit input and returns a 7-bit output signal, and converts a binary number to a 7-segment display encoding.

## Slide 7: Show the Results of the Addition
Show the result of our adder circuit from Lab 2 using the 7-segment display. You need one overflow bit to be displayed on an LED.
Attach an instance of the decoder to the output of the adder.
Hint: Create a new “top” module that will create an instance of each module and make appropriate connections between them.

## Slide 8: Last Words
In Lab 3, you will design more combinatorial circuits.
Convert a binary number to 7-Segment display encoding.
Implement a circuit to drive the 7-Segment display.
Show the addition result on the 7-Segment display.
In the report, you will learn how to display the addition result using only a single 7-segment display.

## Slide 9: Report Deadline
23:59, 3 April 2020

## Slide 10: Digital Design & Computer Arch. Lab 3 Supplement: Verilog for Combinational Circuits
Prof. Onur Mutlu
ETH Zurich
Spring 2020
13 March 2020